## Slide 1: Electronic Devices and Circuits Lecture-8
Prepared by
Ipshita Tasnim Raha
Lecturer (Provisional)
Dept. of CSE
Varendra University
CSE 223

## Slide 2
Operational Amplifier (Op-Amp)

## Slide 3
An operational amplifier (or an op-amp) is an integrated circuit (IC) that operates as a voltage amplifier. It is a differential amplifier that amplifies the difference of voltages applied to its two input terminals (differential input), and provides a single ended output.
These amplifiers are called "operation" amplifiers because they were initially designed as an effective device for performing arithmetic operations in an analog circuit. The op-amp has many other applications in signal processing, measurement, and instrumentation.
Operational Amplifier
Prepared by Ipshita Tasnim Raha
Notes: https://www.youtube.com/watch?v=lACEHw9D7eA&list=PLMjaJoGgWV1keJY9g3rbRaJG4mOj1Dn_Z

## Slide 4
Symbol & Terminals
Prepared by Ipshita Tasnim Raha

## Slide 5
1. Several operation
Addition
Subtraction
Integration
differentiation etc.
2. Active filter
3. Oscillator
4. Waveform convertor
5. ADC & DAC convertors
6. Voltage follower
7. Voltage comparator
Op-Amp Application
Prepared by Ipshita Tasnim Raha

## Slide 6
An OP-AMP has a two input terminal, one output terminal and two supply voltage terminals.
The input terminal marked with negative (-) sign is called as an inverting terminal .If we connect the input signal to this terminal then the amplified output signal is 180º out of phase with respect to input.
The input terminal marked with positive (+) sign is called as Non-Inverting terminal. If the input is applied to this pin then the amplified output is in phase with the input.
+Vs (positive supply) & –Vs (Negative supply) are power supply or biasing voltage.
Offset null is used to nullify the offset voltage and pin no 8 is dummy pin.
Op-Amp terminals
Prepared by Ipshita Tasnim Raha

## Slide 7
Inverting & Non-Inverting input
Prepared by Ipshita Tasnim Raha

## Slide 8
Power Supply (+Vs ,-Vs )
Prepared by Ipshita Tasnim Raha
Vd (differential input signal)
Let, vd = 1mV
So, Vout=Avd= 1*105=100V [the value of gain typically ranges from 105 - 108]

## Slide 9
1. Single ended mode : If the input signal is applied to only one of the inputs and the other input terminal is connected to ground it is said to be operating in single ended mode.
OP-AMP input modes
Prepared by Ipshita Tasnim Raha

## Slide 10
2. Differential mode/double ended: In differential mode ,two opposite polarity signal are applied to the two inputs of op amp. The difference between the input signal is amplified appears at the output
OP-AMP input modes
Prepared by Ipshita Tasnim Raha

## Slide 11
3. Common mode: In the common mode of operation, the same input signal is applied to both the input terminals. Ideally a zero voltage should be produced by the op amp.
OP-AMP input modes
Prepared by Ipshita Tasnim Raha

## Slide 12
The graph that relates the output voltage to the input voltage is called the voltage transfer curve and is fundamental in designing and understanding amplifier circuits.
The voltage transfer curve of the op-amp is shown below
Op-Amp voltage transfer characteristics
Prepared by Ipshita Tasnim Raha

## Slide 13
The importance of a differential amplifier (DA) lies in the fact that the outputs are proportional to the difference between the two input signals. Thus the circuit can be used to amplify the difference between the two input signals or amplify only one input signal simply by grounding the other input. The input signals to a Differential Amplifier (DA) are defined as:
    (i) Common-mode signals (ii) Differential-mode signals
Common-mode and Differential-mode Signals:
Prepared by Ipshita Tasnim Raha

## Slide 14
(i) Common-mode signals : When the input signals to a DA are in phase and exactly equal in amplitude, they are called common-mode signals. The common-mode signals are rejected (not amplified) by the differential amplifier. It is because a differential amplifier amplifies the difference between the two signals (v1 – v2) and for common-mode signals, this difference is zero. In common-mode operations, v1 = v2.
The voltage gain of DA operating in common-mode is called common mode voltage gain and is denoted by ACM.
Ideally ACM = 0
Common-mode and Differential-mode Signals:
Prepared by Ipshita Tasnim Raha

## Slide 15
(ii) Differential-mode signals. When the input signals to a DA are 180° out of phase and exactly equal in amplitude, they are called differential-mode signals. The differential-mode signals are amplified by the differential amplifier. It is because the difference in the signals is twice the value of each signal. For differential-mode signals, v1 = –v2.
The voltage gain of a DA operating in differential mode is called differential-mode voltage gain and is denoted by ADM
Common-mode and Differential-mode Signals:
Prepared by Ipshita Tasnim Raha

## Slide 16
Math Problem
Prepared by Ipshita Tasnim Raha

## Slide 17
Op-Amp Equivalent Circuit
Prepared by Ipshita Tasnim Raha
Notes: Reference book: VK Mehta, PG: 690

## Slide 18
Infinite (∞) voltage gain. ADM = infinite (theoretically)
Input impedance, Ri = ∞
Zero output impedance, R0 =0
Slew rate = ∞ [Slew rate is the maximum rate at which an amplifier can respond to the sudden change of input level]
CMRR = ∞ [The op amp common-mode rejection ratio (CMRR) is the ratio of the differential-mode gain to common-mode gain ]
Bandwidth = ∞
Characteristics of Ideal op-amp
Prepared by Ipshita Tasnim Raha

## Slide 19
A differential amplifier should have high differential voltage gain (ADM) and very low common mode voltage gain (ACM). The ratio ADM /ACM is called common-mode rejection ratio (CMRR). That is,
CMRR = ADM/ACM
Very often, the CMRR is expressed in decibels (dB). The decibel measure for CMRR is given by,
Common-mode Rejection Ratio (CMRR):
Prepared by Ipshita Tasnim Raha
Importance of CMRR:
The CMRR is the ability of a DA to reject the common-mode signals. The larger the CMRR, the better the DA is at eliminating common-mode signals.

## Slide 20
Math Problem
Prepared by Ipshita Tasnim Raha

## Slide 21
Math Problem
Prepared by Ipshita Tasnim Raha

## Slide 22
An OP-amp has an infinite input impedance. This means that there is zero current at the inverting input. If there is zero current through the input impedance, then there must be no voltage drop between the inverting and non-inverting inputs. Therefore, the inverting and non-inverting terminals will be at same potential. This means that the voltage at the inverting input (–) is zero because the other input (+) is grounded. The 0V at the inverting input terminal is referred to as virtual ground. The point A is said to be at virtual ground because it is at 0V but is not physically connected to the ground (VA = 0V).
Virtual Ground concept
Prepared by Ipshita Tasnim Raha

## Slide 23
An Op-Amp can be operated as an inverting amplifier. An input signal vin is applied through input resistor Ri to the minus input (inverting input). The output is fed back to the same minus input through feedback resistor Rf. The plus input (non-inverting input) is grounded. The resistor Rf provides the negative feedback. Since the input signal is applied to the inverting input (–), the output will be inverted as compared to the input. Hence the name inverting amplifier.
Inverting Amplifier
Prepared by Ipshita Tasnim Raha

## Slide 24
According to virtual ground concept, the current I1 to the inverting input is zero. Therefore, current Iin flowing through Ri entirely flows through feedback resistor Rf. In other words,
If = Iin
=
Voltage gain
Prepared by Ipshita Tasnim Raha
Vout=

## Slide 25
Example 1: Given the OP-amp configuration in Figure, determine the value of Rf required to produce a closed-loop voltage gain of –100.
Math Problem
Prepared by Ipshita Tasnim Raha

## Slide 26
Example 2: Determine the output voltage for the given circuit.
Math Problem
Prepared by Ipshita Tasnim Raha

## Slide 27
Non-inverting Amplifier
Prepared by Ipshita Tasnim Raha
There are times when we wish to have an output signal of the same polarity as the input signal. In this case, the OP-amp is connected as non-inverting amplifier. The input signal is applied to the non-inverting input (+). The output is applied back to the input through the feedback circuit formed by feedback resistor Rf and input resistance Ri. This produces negative feedback in the circuit. Here Ri is grounded. Since the input signal is applied to the non-inverting input (+), the output signal will be non-inverted that is, the output signal will be in phase with the input signal.

## Slide 28
Voltage gain
Prepared by Ipshita Tasnim Raha
Two terminals of an Op-Amp remain at same potential. Therefore, the potential at point A is the same as Vin.
Since the input impedance of OP-amp is very high, all of the current that flows through Rf also flows through Ri. Keeping these things in mind, we have, Voltage across Ri = Vin – 0 Voltage across Rf = Vout – Vin
Now, Current through Ri = Current through Rf

## Slide 29
Math Problems
Prepared by Ipshita Tasnim Raha
Example 1: Calculate the output voltage from the non-inverting amplifier circuit of the following circuit for an input of 120 μV.

## Slide 30
Voltage Follower/ Voltage Buffer
Prepared by Ipshita Tasnim Raha
Notes: Reference book: VK Mehta, PG: 699

## Slide 31
Summing Amplifiers
Prepared by Ipshita Tasnim Raha
The circuit shows a three-input summing amplifier circuit, which provides a means of algebraically summing (adding) three voltages, each multiplied by a constant-gain factor
Notes: Reference book: VK Mehta, PG: 699

## Slide 32
Math 2
Prepared by Ipshita Tasnim Raha
Math 1
Notes: Reference book: VK Mehta, PG: 711

## Slide 33
OP-Amp Integrators & Differentiators
Prepared by Ipshita Tasnim Raha
For a differentiator,

## Slide 34: Thanks!
Any questions?